Illustration 1: Variable threads. Problem size n*n where n = 1000
Threads
Time (s)
Report lab 3 – Image Filter (MPI)
# Description
The algorithm calculates a column at a time from left to right until all columns have been updated in each step. Each calculations for the next iteration relies on the old values in the matrix from the previous iteration, so data needs to be saved if it hasn't been utilized previously.
In the sequential algorithm, this is done by copying the current column before calculating its new values. This is also used in the parallel algorithm where each thread is assigned a number of columns which they then iterate over from left to right as in the sequential algorithm. The only difference here is that each thread has to make a copy of the column before its start column and the same for the column after its last. The columns are assigned in the same way that the omp do directive assigns jobs to threads. When all copies have been made, the threads can begin the iteration and when they are calculating their first or last column, they use the copied data.
The error in the parallel algorithm is calculated by taking the max out of all errors between all the threads.
# Execution times
The first test we did we varied the number of threads, keeping the problem size constant at 1000 * 1000. The result we got was expected where the execution time is roughly halved when the number of threads was doubled.
In the second test we did we varied the problem size and kept the number of processes constant. Since the problem size is given by n from which we get a n x n matrix. This leads to a quadratic increase of the problem. From illustration 2 we can pretty clearly see that the execution time increases approximately by 4 times when we double the problem size, which is what we anticipated due to the increase of the matrix size.

Illustration 2: Variable problem size where n = size. Threads are kept at 4.
Data size
Time (s)

In our last test we varied both the number of threads and the problem size. In illustration 3 we can see that we get a linear development when we double both variables at the same time. From what we got from the first two tests where the threads gave a linear speed up and size gave a quadratic slow down, a linear slow down is expected.

T = threads s = data size
Time (s)
Illustration 3: Both size and thread count variable. T = threads and s = size where n = size.
# Appendix

Table 1: Variable threads. Problem size n*n where n = 1000

Table 2: Variable problem size where n = size. Threads are kept at 4.

Table 3: Both size and thread count variable. T = threads and s = size where n = size.